## Slide 1: Transforming Transportation in Plano

## Slide 2: Transportation Division Priorities
Safety
Moving traffic
Reliability
Transparency & user input
Leverage technology & funding
Notes: Transparency & User Input
  Transportation Website
  Value User Recommendations & Service Requests
  Citizen’s Academy
Leverage Technology
  Effective Real-Time Traffic Management
  Continuous Improvement

## Slide 3: Traffic Safety
Annual HAL/HARS Analysis
  Reported crashes of last calendar year
  Crash categorization
  Location mapping with GIS
  Incorporates neighboring cities data
  Identifies locations for improvements
Notes: Requires extensive data clean up
  CRIS data is only as good as the cop that wrote the report
  Cleaning up location, as well as several other parameters
Recently added unsignalized and midblock analysis
Segregate the highway crashes

## Slide 4: Traffic Safety – Case Study
2 Box Diamonds
  Preston Road @ SH 121
  Dallas Parkway @ SH 121
  Highest crash locations in City
  Geometry and signal phasing concerns
  Signal timing revised to TTI 4-phase
  Interior Crash reduction of over 75%

## Slide 5: The Transformation
TRAFFIC MANAGEMENT
CENTER**
Vehicle Detection System
CCTV System
Emergency Vehicle Preemption System
Communications
System
Intersection Traffic Control System
Performance Measurement System
Traffic Signal System
School Zone Flasher System
LEGEND
- Recently Upgraded System
- Expanding System
- Upgrading System
- Assess New/Upgrade Options
** - Daily activities include identifying, trouble-shooting, and addressing system problems; developing, implementing, and fine-tuning coordinated traffic signal timing; accident analysis; developing/updating mapping and inventory systems; coordinating with other agencies and City departments; and addressing citizen requests.
Notes: Most equipment was over 15 years old.
Master Plan

## Slide 6: School Zone Flasher System
Historical Issues
Project Overview
  180+ school-zone flashers
  Applied Information GLANCE System
  Positive command and control
  Vendor-hosted Cellular Communication
  10-year service contract
Project Cost ~ $630,000
Project Completed 2018
Notes: Former System
  “Dumb” Clocks
  Significant Field-crew effort required
  Twice a year manual programing
  Reliant on Citizen calls when not operating correctly
Funding Source: Traffic Safety Fund (Red Light Camera)

## Slide 7: Emergency Preemption
Project Overview
  Implement secure coded system
  Prevent unauthorized use
  Reduce impacts to timing coordination
  Upgrade phase selectors
  Coordinate with other agencies
Project Benefits
  20% reduction in preempt calls
Project Cost ~ $330,000
Project Completed 2020
Notes: Concern was…
Stealing the green
Upgrade phase selectors to Ethernet
Project cost was largely hardware, but also included a new central software

## Slide 8: CCTV System
Project Overview
  Provide real-time video
  Establish data sharing agreements
PS&E design by consultant
Construction by contractor
Total Estimated Cost ~ $3.3M
Project Completion ~ 2024
Notes: 2 different projects for funding
  44 cameras existing
160 cameras with first project design is almost done
80 cameras with next project this design contract hasn’t been executed yet.

## Slide 9: Vehicle Detection System
Historical Issues
Project Objectives
  Develop reliable vehicle detection toolbox
  Support high resolution data
  Provide ATSPM/Purdue functionality
  Provide live video feeds to TMC
  Allow real-time adjustment to detection
Spec Development by Consultant
Detection Programming by City staff
Estimated Cost ~ $8.3M
Project Completion ~ 2024
Notes: VIVDS system is largely autoscope solopro analog has reached end of life.
Frankenstien maintenance at this point
Trafficware Pods were installed as a pilot adaptive system and those were a total failure
Issues with Video Detection we get a lot of false calls and dropped called

## Slide 10: Intersection Traffic Control System
EXISTING SYSTEM
CalTrans 332 cabinets
TrafficWare 2070 controllers
Autoscope VIVDS
GTT IR Opticom with central monitoring
ATMS.now central system
Limited CCTV coverage
100% ethernet communication
  Cradlepoint LTE 55%
  City-Owned Fiber Network 45%
  97%+ uptime
Notes: CalTrans 332 cabinets
  Limited 20-channel cabinets
  Limited BBU coverage

## Slide 11: Intersection Traffic Control System
Project Overview
  Develop new City standard:
    Local controller software
    Local controller hardware
    ATC traffic cabinets
    New central management system
  Allow for improved phasing/timing plans
  Modernized equipment
Spec development by consultant
Implementation and deployment largely by City forces
Estimated Cost ~ $7.4M
Estimated Completion ~ 2024

## Slide 12: Performance Measurement System
Project Overview
  New central system software
  Real time ATSPM reporting
  Real time timing adjustments
  Collect real time traffic counts
Specifications by consultant
Implementation and maintenance by City staff
Estimated Cost ~ $1.2M
Project Completion ~ 2025

## Slide 13: New Traffic Signals
Project Overview
  10 new traffic signals under design
City consultant designing 8 signals
Private developer installing 2 signals
Estimated Cost ~ $2.8M
Project Completion 2022-2023

## Slide 14: Communications System History
CATV - Analog (Pre 2000)
900 MHz Spread Spectrum Radio (2000-2016)
Wireless MotoMesh Network (2014-2020)
Notes: CATV - Analog (Pre 2000)
  Supported analog PTZ Cameras
  B-Side Plant decommissioned by Cable Company
900 MHz Spread Spectrum Radio (2000-2016)
  Repeaters on water towers, City hall, and a leased AT&T tower
  Limited Bandwidth, No CCTV support
  Line of Sight Issues
Wireless MotoMesh Network (2014-2020)
  Ethernet connectivity
  Limited Bandwidth, Poor Performance
  Line of Sight Issues
Cradlepoint 4G LTE (2015-Future)
Fiber Network (2019-Future)

## Slide 15: Communications System History
CATV - Analog (Pre 2000)
900 MHz Spread Spectrum Radio (2000-2016)
Wireless MotoMesh Network (2014-2020)
Cradlepoint 4G LTE (2015-Future)
Fiber Network (2019-Future)
Notes: CATV - Analog (Pre 2000)
  Supported analog PTZ Cameras
  B-Side Plant decommissioned by Cable Company
900 MHz Spread Spectrum Radio (2000-2016)
  Repeaters on water towers, City hall, and a leased AT&T tower
  Limited Bandwidth, No CCTV support
  Line of Sight Issues
Wireless MotoMesh Network (2014-2020)
  Ethernet connectivity
  Limited Bandwidth, Poor Performance
  Line of Sight Issues
Cradlepoint 4G LTE (2015-Future)
Fiber Network (2019-Future)

## Slide 16: Communications System Upgrades
Project Overview
  Connect majority of network to City fiber
  Inter-local sharing agreements
  Maintain >97% uptime
PS&E design by consultants
Construction by contractor
Estimated Cost ~ $4.9M
Project Completion ~ 2025
Notes: Adds another 110 signals to the network

## Slide 17: Traffic Management Center
Estimated Cost ~ $457,000
Estimated Completion Date ~ Late Fall 2022
Notes: Supply chain issues
Substantially complete

## Slide 18: Other Projects
DART Silver Line
  Coordination
  Railroad preemption
Thoroughfare standards update
  Traffic calming
City wayfinding
System wide signal retiming
CIP intersection improvements
Minor traffic operations improvements
Notes: TIA requirements and Loopholes to thoroughfare standards
Intersection improvements informed by HAL HARS

## Slide 19: Funding Sources
CIP (City Bond Funding) $29,572,000
Federal – CMAQ $2,269,000
Federal – ARPA $9,800,000
Red Light Running Funds $1,417,000
Total Funds Allocated $43,058,000
Notes: CMAQ – CCTV and a few signal cabinets
ARPA – Vehicle Detection and Wayfinding
Red Light Funds – TMC, Opticom, School Zone Flashers

## Slide 20: Engineering Opportunities
Open positions: Plano.gov/Jobs
  Senior Traffic Engineer / Traffic Engineer (PE)
  Senior Transportation Technician (TMC Operator)
Existing consultant contracts
  $3.7M contracted consultant fees 2019 – Present
  10 different firms over 18 projects
Future consultant contracts
  At least $2.5M in planned traffic engineering contracts
  RFQ for on-call services late summer 2022

## Slide 21: Questions
Matt Tilke
  mtilke@plano.gov
  972-941-5765
Chad Ostrander
  costrander@plano.gov
  972-941-5341